## Slide 1
Start
Prepare basic geometry in NX 12
IGES file
Prepare geometry in Marc Mentat
Randomly delete internal element(s)
Run non-linear simulation
Verify and interpret results
All possible internal geometries tested?
Useful and meaningful results
Internal geometry already tested?
End

## Slide 2
Prepare basic geometry in NX 12
Open Siemens NX 12
Start
File > Utilities > Select Bundles > ACD30 & ACD31
New > Model
Sketch > XY plane
Rectangle > Origin > 5 > 5
Finish Sketch
Save
Surface > Fill Surface > Select all curves
File > Export > IGES
End

## Slide 3
Prepare geometry in Marc Mentat
Open Marc Mentat 2019
Start
File > Import > IGES File
Save
Operations > Sweep > All
Basic Manipulation > Renumber > All geometry and mesh
Pre-Automesh > Curve Divisions
Boundary Conditions > New (Structural) > Fixed Displacement
Automesh > Planar
File > Export > IGES
End
Fill view
Tables > New > 1 Independent Variable