## Slide 1
Start
1. Prepare basic geometry in NX 12
2. IGES file
3. Prepare geometry in Marc Mentat
4. Randomly delete internal element(s)
6. Run non-linear simulation
7. Verify and interpret results
9. All possible internal geometries tested?
8. Useful and meaningful results
5. Internal geometry already tested?
End

## Slide 2
1. Prepare basic geometry in NX 12
1.1. Open Siemens NX 12
Start
1.2. File > Utilities > Select Bundles > ACD30 & ACD31
1.3. New > Model
1.4. Sketch > XY plane
1.5. Rectangle > Origin > 5 > 5
1.6. Finish Sketch
1.8. Save
1.7. Surface > Fill Surface > Select all curves
1.9. File > Export > IGES
End

## Slide 3
Prepare geometry in Marc Mentat
Open Marc Mentat 2019
Start
File > Import > IGES File
Save
Operations > Sweep > All
Basic Manipulation > Renumber > All geometry and mesh
Pre-Automesh > Curve Divisions
Boundary Conditions > New (Structural) > Fixed Displacement
Automesh > Planar
Boundary Conditions > New (Structural) > Edge Load
End
Fill view
Tables > New > 1 Independent Variable
Geometric Properties > New (Structural) > Plane Strain
Material Properties > New > Finite Stiffness Region > Standard